## Slide 1: APEX 2015 Summary
Matthew O’Kelly, Houssam Abbas, Rahul Mangharam

## Slide 2: Motivation

## Slide 5: Summary of Current Work
Target Vehicle
Road Network
Traffic Laws
Other Drivers
Pedestrians
Infrastructure
Driving Scenario
Map driving scenarios to collections of agents represented as hybrid systems
Implement state-lattice
planning stack in C++
Validation of algorithms & software
1
2
3
4
5
Integrate ROS based vehicle OS
6
7
Explore the modeling of subsets of autonomous driving missions as scenarios
APEX automatically generates and solves a tree of reachability problems
Solution:
Reachability Problem
How can we provide a driver’s license for autonomous vehicles?

## Slide 6: Summary of Current Work
Development of AV model
Development of hybrid systems framework to accommodate AV model
Development of tools to automatically generate model checkable scenarios
Expansion of modeling framework to incorporate more sources of uncertainty
Benchmark creation and uncertainty analysis
Development of framework for scenario creation from Open Street Maps.
Support for AV model in Unity and Rviz.

## Slide 7: Modeling Part 1

## Slide 8: Basic Architecture

## Slide 9: Vehicle Model
The bicycle model to is used as the intermediate representation (IR) because it supports verification of low level trajectory trackers and analysis with respect to first order logic necessary for formal verification.

## Slide 10: Trajectory Generation
Local Planner
(C++ Implementation)
400ms
600ms
700ms
Time
Trajectory 1
Trajectory 2
Trajectory 3
Trajectory 4
Trajectory 5
Trajectory 6
Trajectory 7
Trajectory 8
Choosing a Single trajectory
Every 100ms by Cost Function
Trajectory 1
Trajectory 2
Trajectory 3
Trajectory k
Trajectory n
Trajectory k
System
Start
(Local planner generates multiple trajectories every 100ms)
(Local planner choose one best trajectory every 100ms)

## Slide 11: Behavior Controller: Two Representations
Initially, a ego vehicle is in the lane following mode (LF);
If a relative speed of the ego vehicle is greater than the ahead vehicle’s speed by a certain threshold (ϵ), and the distance from the ahead vehicle is less than a certain threshold (buffer), the behavioral planner change the model from the lane following (LF) to lane change (LC);
In the lane changing mode (LC), the behavioral planner will instruct the local planner to generate trajectories to change the lane;
Once the ego vehicle changes the lane successfully, the behavioral planner change the mode from lane keeping to the lane following model

## Slide 12: Behavior Controller: Two Representations
Initially, a ego vehicle is in the lane following mode (LF);
If a relative speed of the ego vehicle is greater than the ahead vehicle’s speed by a certain threshold (ϵ), and the distance from the ahead vehicle is less than a certain threshold (buffer), the behavioral planner change the model from the lane following (LF) to lane change (LC);
In the lane changing mode (LC), the behavioral planner will instruct the local planner to generate trajectories to change the lane;
Once the ego vehicle changes the lane successfully, the behavioral planner change the mode from lane keeping to the lane following model

## Slide 13: Scenario 1

## Slide 14: Simple Lane Change

## Slide 15: Specification

## Slide 16: Verification Algorithm

## Slide 17: dReach Verification Instance
//Trajectory
#define s (22.681867) #define kappa_0 (0.000000) #define kappa_1 (0.033194)
#define kappa_2 (-0.033194) #define kappa_3 (0.000000)
// Constants
#define m 2273.0 #define Iz 4423.0 #define Cf 108000.0 #define Cr 108000.0
#define lf 1.292 #define lr 1.515 #define k1 2.0 #define k2 12.0 #define k3 4.0
#define k4 2.0 #define k5 1.0 #define k6 10.0
// Scenario parameters
#define w 3.7 // Width of road
#define v_d 11.11 // Desired velocity
#define a_env 0.0 // Acceleration of environmental vehicle.
// Helpers to clean up equations...
#define cl (Cr*lr-Cf*lf)
// Tracking controller inputs
// Rate of change of front wheel angle
#define vw k1*(cos(Psi_d)*(sy_d - sy) - sin(Psi_d)*(sx_d - sx)) +k2*(Psi_d - Psi) +k3*(Psi_dot_d - Psi_dot) -k4*(delta)
// Longitudinal acceleration
#define ax k5*(cos(Psi_d)*(sx_d - sx) + sin(Psi_d)*(sy_d - sy)) +k6*(v_d-v)
// Cubic spline inputs
#define a (kappa_0)
#define b ((-0.50)*(-2*kappa_3 + 11*kappa_0 - 18*kappa_1 + 9*kappa_2)/s)
#define c ((4.50)*(-kappa_3 + 2*kappa_0 - 5*kappa_1 +4*kappa_2)/(s*s))
#define e ((-4.50)*(-kappa_3 + kappa_0 - 3*kappa_1 + 3*kappa_2)/(s*s*s))
// Bounds on variables
[0,3.1] tau; [-2,2.03] Beta; [-2,2.04] Psi; [-2,2.05] Psi_dot;
[6,12] v; [0,50] sx; [0,10] sy; [-2, 2.04] delta; [0, 3.1] time;
[-2,2.06] kappa_d; [-2,2.07] Psi_d; [0,50] sx_d; [0,10] sy_d; [-2,2.08] Psi_dot_d;
[9, 50] sx_env;
// Dynamics
{
// Lane change motion primitive
mode 1;
invt:
// X position must be greater than or equal to 0
(sx>=0);
// Velocity must be greater than or equal to 0
(v>=0);
flow:
/* TARGET VEHICLE */
/* Plant equations */
d/dt[tau]=1; // Time
// Compute rate of change of the slip angle
d/dt[Beta]=((cl/(m*v*v))-1.0)*Psi_dot + Cf*delta/(m*v) - (Cf+Cr)*Beta/(m*v);
d/dt[Psi]=Psi_dot; // Rate of change of the heading angle is equal to yaw rate
// Rate of change of yaw rate
d/dt[Psi_dot]=(cl*Beta/Iz) - ((lf*lf*Cf+lr*lr*Cr)/Iz)*(Psi_dot/v) + (lf*Cf)*delta/Iz;
d/dt[v]=ax; // Longitudinal acceleration
d/dt[sx]=v*cos(Beta+Psi); // X component of velocity
d/dt[sy]=v*sin(Beta+Psi); // Y component of velocity
d/dt[delta]=vw; // Rate of change of front wheel angle.
/*Trajectory and Tracking Equations*/
d/dt[kappa_d] = b*v_d + 2*c*v_d*v_d*tau + 3*e*v_d*v_d*v_d*tau*tau ;
d/dt[Psi_d] = v_d*kappa_d;
d/dt[sx_d] = v_d*cos(Psi_d);
d/dt[sy_d] = v_d*sin(Psi_d);
d/dt[Psi_dot_d] = v_d*(b*v_d + 2*c*v_d*v_d*tau + 3*e*v_d*v_d*v_d*tau*tau);
// Other Vehicle
d/dt[sx_env]=0.0;
jump:
}
init:
@1 (and (sx>=0) (sx<=0.5) (sy>=0) (sy<=0.1) (v>=10.8) (v<=11.1) (sx_d=0) (sy_d=0)
(Psi>=0) (Psi<=0.01) (Psi_dot=0) (Beta=0) (delta=0) (tau=0)
(Psi_d=0) (Psi_dot_d=0)
(sx_env=15) (kappa_d=0));
goal:
@1 (or (and (sy<w) (tau>2) (tau<3)) (and (sy<w) (sx>sx_env)));
An example dReach file that is automatically converted from one trajectory generated from the local planner

## Slide 18: Simple Lane Change
Scenario
  The vehicle ahead suddenly stops during lane following
Verification Result: SAT (Unsafe)
  (i.e.) the vehicle may crash the ahead vehicle)
Analysis (Based on the counter example)
  Buffer (15m) is too small to change the lane
  Initial position of the vehicle is heading slightly toward right before starting lane changing
  The dotted line shows the intended trajectory, the solid line shows the actual trajectory
  Error due to poor state estimation
Symbol | Note | Old Assignment | New Assignment
w | Lane Width | - | 3.7m
ε | Threshold of the relative speed | - | 1 m/s
Buffer | Distance from the ahead vehicle | - | 15 m
tf | Max timestep to generate the trajectories | - | 3.0 s
V | Velocity of Ego Vehicle | - | [10.8, 11.1]
Sx | Position of Ego Vehicle, X | - | [0.0, 0.5]
Sy | Position of Ego Vehicle, Y | - | [0.0, 0.1]
Φ | Orientation of Ego Vehicle, rad | - | [0.0, 0.1]

## Slide 19: Simple Lane Change: Part 2
Symbol | Note | Old Assignment | New Assignment
w | Lane Width | 3.7m | 3.7m
ε | Threshold of the relative speed | 1 m/s | 1 m/s
Buffer | Distance from the ahead vehicle | 15 m | 20 m
tf | Max timestep to generate the trajectories | 3.0 s | 3.0 s
V | Velocity of Ego Vehicle | [10.8, 11.1] | [10.9, 11]
Sx | Position of Ego Vehicle, X | [0.0, 0.5] | [0.0, 0.5]
Sy | Position of Ego Vehicle, Y | [0.0, 0.1] | [0.0, 0.05]
Φ | Orientation of Ego Vehicle, rad | [0.0, 0.1] | [0.0, 0.1]

## Slide 20: Simple Lane Change: Part 3
Symbol | Note | Old Assignment | New Assignment
w | Lane Width | 3.7m | 3.7m
ε | Threshold of the relative speed | 1 m/s | 1 m/s
Buffer | Distance from the ahead vehicle | 15 m | 20 m
tf | Max timestep to generate the trajectories | 3.0 s | 3.0 s
V | Velocity of Ego Vehicle | [10.8, 11.1] | [10.9, 11]
Sx | Position of Ego Vehicle, X | [0.0, 0.5] | [0.0, 0.5]
Sy | Position of Ego Vehicle, Y | [0.0, 0.1] | [0.0, 0.05]
Φ | Orientation of Ego Vehicle, rad | [0.0, 0.1] | [0.0, 0.2]

## Slide 21: Results: Composition of Trajectories

## Slide 22: Results: Parallelization of Search

## Slide 23: Results: Infinite Time Property

## Slide 24: Complexity and Results

## Slide 25: Modeling Part 2

## Slide 26: Pure Pursuit

## Slide 27: Pure Pursuit

## Slide 28: Sources of Non-Determinism

## Slide 29: Differential Inclusions
[0, 20] x;
[-9.8] g;
[-100, 100] v;
[0, 10] time;
[-1, 1] noise [2.0];
{ mode 1;
invt:
(v <= 0);
(x >= 0);
flow:
d/dt[x] = v + noise;
d/dt[v] = g + noise;
d/dt[noise] = 0;
jump:
(x = 0) ==> @2 (and (x' = x) (v' = (0 - v)));
}
In order to model uncertainty we can add noise terms to the dynamics of various agents.
For example a priori environmental agents may accelerate at any rate within a specified interval.
Furthermore, the measurement of certain state variables of the ego vehicle may be subject to sensor noise.
If we are to design robust robotic systems it is desirable to verify the design under the presumption that any of these conditions may prevail at any time.

## Slide 30: Scenario 2

## Slide 31: Simple Lane Change

## Slide 32: Specification

## Slide 33: Variations

## Slide 34: Complexity and Results

## Slide 35: APEX Tool

## Slide 36: Map Manipulation

## Slide 37: Reference Trajectory Generation

## Slide 38: Traffic Control

## Slide 39: Agents

## Slide 40: File Generation

## Slide 41: Counterexamples

## Slide 42: Interfacing AV Infrastructure
Wrapper for trajectory generation software so that it may be used with Unity.
Link:
How to:

## Slide 43: F1\10?

## Slide 44: Vehicle

## Slide 45: Demo

## Slide 46: Next Steps

## Slide 47: Next Steps: Proactive Driver Assistance

## Slide 48: Summary